## Slide 2: Two microarchitecture techniques
Caches
Keep “useful” things closer to processor

## Slide 3: Two microarchitecture techniques
 | Way 0 | Way 1
Set 0 |  | 
Set 1 |  | 
Set 2 |  | 
Set 3 |  | 
0xAB140
0xAB140
0xAB140
0xAB180
0xAB180
0xAB180
0xAB140
0xAB140
Caches
Keep “useful” things closer to processor

## Slide 4: Two microarchitecture techniques
Caches
Keep “useful” things closer to processor
Out of order execution
Instructions can execute even if previous instructions haven’t
 | Way 0 | Way 1
Set 0 |  | 
Set 1 |  | 
Set 2 |  | 
Set 3 |  | 
0xAB140
0xAB180
0xAB140
0xAB140
Cache hits are fast and misses are slow

## Slide 5: Two microarchitecture techniques
Out of order execution
Instructions can execute even if previous instructions haven’t
mov %rax, [%rcx]
cmp %rax, %rbx
jge END
mov %rcx, [%rbx]
size = *size_ptr;
if (x < size) {
y = array[x];
}

## Slide 6: Two microarchitecture techniques
Caches
Keep “useful” things closer to processor
Cache hits are fast and misses are slow
Out of order execution
Instructions can execute even if previous instructions haven’t
Can speculate, but will always “commit” correctly
mov %rax, [%rcx]
cmp %rax, %rbx
jge END
mov %rcx, [%rbx]
size = *size_ptr;
if (x < size) {
y = array[x];
}

## Slide 7
Virtual memory
0x00000000
0xFFFFFFFF
Code
Heap
Stack
Kernel Space
0xC0000000
char *addr = 0xFFFF0000;
char *array[256 * 512];
char temp = 0xFF;
char secret = *addr;
temp &= array[secret];

## Slide 8
retry:
mov al, [rcx]
shl rax, 0xc
jz retry
mov rbx, [rbx + rax]
...
https://github.com/IAIK/meltdown
char *addr = 0xFFFF0000;
char *array[256 * 512];
char temp = 0xFF;
char secret = *addr;
temp &= array[secret];
rcx
rbx
rax

## Slide 9
retry:
mov al, [rcx]
shl rax, 0xc
jz retry
mov rbx, [rbx + rax]
...
 | Way 0 | Way 1
Set 0 |  | 
Set 1 |  | 
Set 2 |  | 
Set 3 |  | 
. . . |  | 
...
for (i=0; i<256; i++) {
t = time(array[i])
if (t < 80) // Hit!
...
char *addr = 0xFFFF0000;
char *array[256 * 512];
char temp = 0xFF;
char secret = *addr;
temp &= array[secret];

## Slide 10
https://www.youtube.com/watch?v=RbHbFkh6eeE

## Slide 11: Similar attacks
Meltdown: Ignores page table permissions
LazyFPU: Ignores floating point disabled
Foreshadow or L1 terminal fault: Ignores lots of permissions
Virtual machine
Security extensions (SGX)
Others???

## Slide 12: Assumptions
Every instruction executes “atomically”
Permissions checks may happen late
Memory operations take the same amount of time
Caches are not invisible
mov al, [rcx]
Notes: Write: Key problem: difference between architectural state and microarchitectural state
What is this???

## Slide 13
void victim_function(size_t x) {
if (x < array1_size) {
temp &= array2[array1[x] * 512];
}
}
size_t array1_size = 16;
uint8_t array1[array1_size] = {0,1,2,...,15};
uint8_t array2[256 * 512];
Notes: Introduce branch prediction here!

## Slide 14
https://gist.github.com/ErikAugust/724d4a969fb2c6ae1bbd7b2a9e3d4bb6
void victim_function(size_t x) {
if (x < array1_size) {
temp &= array2[array1[x] * 512];
}
}
Notes: We’ll come back to this in a minute, but first, let’s simplify further.
So, this code is put through a compiler, and assembly/instructions are generated.

## Slide 15
https://gist.github.com/ErikAugust/724d4a969fb2c6ae1bbd7b2a9e3d4bb6
000000000040105e <victim_function>:
40105e: push %rbp
40105f: mov %rsp,%rbp
401062: mov %rdi,-0x8(%rbp)
401066: mov 0x2bf014(%rip),%eax
40106c: mov %eax,%eax
40106e: cmp -0x8(%rbp),%rax
401072: jbe 40109f <victim_function+0x41>
401074: mov -0x8(%rbp),%rax
401078: add $0x6c00a0,%rax
40107e: movzbl (%rax),%eax
401081: movzbl %al,%eax
401084: shl $0x9,%eax
401087: cltq
401089: movzbl 0x6c1d80(%rax),%edx
401090: movzbl 0x2e0ce9(%rip),%eax
401097: and %edx,%eax
401099: mov %al,0x2e0ce1(%rip)
40109f: pop %rbp
4010a0: retq
void victim_function(size_t x) {
if (x < array1_size) {
temp &= array2[array1[x] * 512];
}
}
Notes: Explain this is called in a loop. First with x values in the range to warmup the BP then with one outside the range.

## Slide 16
000000000040105e <victim_function>:
40105e: push %rbp
40105f: mov %rsp,%rbp
401062: mov %rdi,-0x8(%rbp)
401066: mov 0x2bf014(%rip),%eax
40106c: mov %eax,%eax
40106e: cmp -0x8(%rbp),%rax
401072: jbe 40109f <victim_function+0x41>
401074: mov -0x8(%rbp),%rax
401078: add $0x6c00a0,%rax
40107e: movzbl (%rax),%eax
401081: movzbl %al,%eax
401084: shl $0x9,%eax
401087: cltq
401089: movzbl 0x6c1d80(%rax),%edx
401090: movzbl 0x2e0ce9(%rip),%eax
401097: and %edx,%eax
401099: mov %al,0x2e0ce1(%rip)
40109f: pop %rbp
4010a0: retq
401072: jbe 40109f <victim_function+0x41>
401089: movzbl 0x6c1d80(%rax),%edx
40107e: movzbl (%rax),%eax
if (x < array1_size)
load array1_size
load array1[x]
load array2[array1[x] * 512]
Modifies addresses present in L1 cache
401066: mov 0x2bf014(%rip),%eax
void victim_function(size_t x) {
if (x < array1_size) {
temp &= array2[array1[x] * 512];
}
}
Notes: Go faster

## Slide 17
Time
if (x < array1_size)
load array1_size
load array2[array1[x] * 512]
load array1[x]
Branch correctly predicted
http://bit.ly/gem5-spectre
Notes: Add: BRANCH CORRECTLY PREDICTED NOT TAKEN

## Slide 18
Time
Branch incorrectly predicted
if (x < array1_size)
load array1_size
load array2[array1[x] * 512]
load array1[x]
Notes: Add: BRANCH INCORRECTLY PREDICTED NOT TAKEN

## Slide 19: Similar attacks
Spectre v1: ignores bounds check
Spectre v2: jumps to random locations
Spectre v4: forwards store data incorrectly
Many, many others
Notes: We’ll come back to this in a minute, but first, let’s simplify further.
So, this code is put through a compiler, and assembly/instructions are generated.

## Slide 20: Assumptions
Instructions execute in order
Can “predict” what code to execute
Memory operations take the same amount of time
Caches are not invisible
Notes: Again add “assumpt8ion” “actually” here. Also may the first picture better?